## Slide 1: Cover Page
Problem Statement/ Concept Title
Smart Helmet Light: auto lights, crash alert and ride log for two-wheeler riders
Theme
[Theme as registered on portal]
Team Name (Registered on portal)
[Team Name]
Team ID (Registered on portal)
[Team ID]
State/UT
[State/UT]
Auto night lights
Crash alert + SMS
Ride session log
Notes: Fill the four bracketed fields from the portal registration. The three icons on the right are the three features: auto night mode, crash detection with SMS alert, and session tracking.

## Slide 2: Problem – Proposed Solution
[Team Name]
CORE PROBLEM
≈9
two-wheeler rider deaths every hour in India (2023)
45%
of all road deaths are two-wheeler riders (2023)
69%
of road deaths happen in rural India (2023)
Source: MoRTH data, analysis in ref. [2]
PROPOSED SOLUTION: ONE ESP32 HELMET + THE RIDER’S PHONE
Auto night mode
LDR senses dusk; front warm-white and rear red lights switch on
Fixes: Low visibility
Crash alert
Impact + stillness → 10 s buzzer → SMS with GPS to contact
Fixes: Nobody calls for help
Session tracking
BLE to phone: route, duration, distance, hard braking
Fixes: No ride record
INNOVATION AND UNIQUENESS
Phone provides GPS + SMS: no SIM or GPS module in the helmet
10 s cancel window and stillness check cut false alarms
Indicative parts cost ₹1,500–2,000; open-source
Notes: Problem: two-wheeler riders are the largest group of road-death victims and most deaths are in rural areas where help is far. Solution: three features on one low-cost helmet add-on. Novelty: the helmet stays cheap because the phone supplies GPS and cellular SMS. Cost figure is an indicative estimate, confirm with your own bill of materials.

## Slide 3: Technical Approach
[Team Name]
INPUTS
HELMET CONTROLLER
OUTPUTS
LDR + 10 k
MPU6050 IMU
NEO-6M GPS (optional)
ESP32
Night mode
Crash state machine
Hard-brake detector
BLE server
WS2812B ×3 front · rear · amber
Buzzer
BLE
Android app (Kotlin): BLE · phone GPS · SMS · session log
Spike ≥ 4 g
Still 2 s
Buzzer 10 s
Cancel?
SMS + GPS
Crash flow
TECHNOLOGIES
C++ / Arduino-ESP32 (PlatformIO)
Kotlin, Android BLE + SmsManager
JSON over BLE GATT
GITHUB / GITLAB
github.com/[user]/smart-helmet-light
DEMO VIDEO
[video link]
EXTENT OF AI TOOLS
Claude: code scaffolding, docs, slides. Team: wiring, testing, review [edit to match]
Notes: Block diagram: sensors on the left feed the ESP32, which drives the lights and buzzer and talks BLE to the Android app. The chevron row is the crash flow. Replace the GitHub, demo video and AI-tools placeholders with your real details.

## Slide 4: Impact Potential
[Team Name]
Impact on target audience
Daily commuters and night riders
Delivery and gig riders
Rural and highway riders
45%
of road deaths are two-wheeler riders (2023) [1][2]
Benefits (social, economic)
Social
Visible at dusk and night
Help alerted automatically
Ride data for safer habits
Economic
Indicative ₹1,500–2,000
Reuses the rider’s phone
Stakeholders
Riders
Families / emergency contacts
Delivery fleets and employers
Road-safety bodies, traffic police
Helmet makers
Notes: Two-wheeler riders account for 45% of road deaths per MoRTH data (2023). The cost figure is indicative. Stakeholder list is where pilots could start: delivery fleets are an obvious first user group.

## Slide 5: Feasibility and Risk Analysis
[Team Name]
FEASIBILITY
Off-the-shelf, low-cost parts
Detector logic tested on a PC: 8 of 8 scenarios pass
Open-source stack, MIT licence
Works with any Android 8.0+ phone
Status: [prototype stage – edit]
Potential challenge / risk | Strategy to overcome it
False alarms (potholes, drops) | 4 g spike + stillness check; 10 s cancel window
BLE link drops after a crash | Phone timer still sends the SMS
No phone, signal or SMS credit | Buzzer + amber lights still warn; limit stated
Thresholds need field tuning | All values in config.h; tune with replay traces
Battery and LED current | Brightness capped; protected TP4056 + Li-ion
Notes: Be upfront: thresholds are starting values until field tested. The phone-side timer is the safety net if Bluetooth drops after the crash. Update the status line to describe what you have actually built and tested.

## Slide 6: Team
[Team Name]
TEAM COMPOSITION AND ROLES
[Member name]
Embedded firmware
ESP32, sensors, LEDs
[Member name]
Phone app
BLE, GPS, SMS, logging
[Member name]
Hardware
Wiring, power, mounting
[Member name]
Research and pitch
Data, deck, demo
CHALLENGES
Telling a crash from a pothole
Keeping the SMS reliable if BLE drops
Powering LEDs and ESP32 from one cell
OUR JOURNEY
[Add 2–3 short lines: how the idea started, tests done, what you learned]
Notes: Fill in the member names and adjust the roles to match who actually did what. The journey box is for your own story.

## Slide 7: References
[Team Name]
[1]
Ministry of Road Transport and Highways, Road Accidents in India 2023 (Transport Research Wing), morth.nic.in
[2]
Newslaundry, “More two-wheelers, gig workers under pressure: In India, 9 bike riders die every hour”, 10 Nov 2025 (analysis of MoRTH data), newslaundry.com
[3]
InvenSense (TDK), MPU-6000 / MPU-6050 Product Specification and Register Map
[4]
Espressif, Arduino-ESP32 documentation (BLE library), docs.espressif.com/projects/arduino-esp32
[5]
Adafruit, NeoPixel Überguide (WS2812B power and wiring), learn.adafruit.com/adafruit-neopixel-uberguide
[6]
NanJing Top Power, TP4056 1 A Standalone Linear Li-Ion Battery Charger datasheet
[7]
Android Developers: Bluetooth LE overview, SmsManager, Foreground services, developer.android.com
[8]
Project repository: code, docs, sample data (synthetic), github.com/[user]/smart-helmet-light
Sample data in the repository is synthetic. Thresholds are starting values pending field tests.
Notes: Replace the repository placeholder with your public GitHub link once it is pushed.